## Slide 1: CIRCUITS

## Slide 31: NOTE:
Read more about The Don’t care cases as used in Karnaugh maps.

## Slide 55: ROMS AND PLA’S
ROM (Read Only Memory)
Its circuit is equivalent to a decoder. It outputs all possible mini-terms of the inputs followed by an encoder.
The output combinations are permanently embedded in its circuitry and the inputs serve to select one of these combinations. Each output is obtained by disconnecting the OR inputs from the AND gates whose mini-terms are not to be included in the output.
Because a ROM must produce all the possible mini-terms its decoder portion is fixed by n (the number of inputs). The encoder portion depends on both the outputs and the way in which all the outputs of a decoder are used to generate the final ROM outputs.

## Slide 61: Sequential Circuits
.

## Slide 62: SEQUENTIAL LOGIC & COMPUTER CIRCUITS
In sequential circuits, the output depends on the current input as well as past output/outputs (current state).
Whereas in combinatorial circuits the output depends only on the present values of the input, at any instant of time.
Sequential circuit can be considered as combinational circuit with feedback circuit.
Sequential circuit uses a memory element as feedback circuit in order to store past values.
The information stored in sequential circuits represents current state of the circuit.
The current state and current input will define output and the next state of the circuit.

## Slide 64: Examples of sequential circuits
Counting device
Memory circuit

## Slide 65: SEQUENTIAL LOGIC & COMPUTER CIRCUITS
Time in a sequential circuit takes on a significant role.
A sequential network is defined according to its inputs and outputs over a period of time.
In sequential networks, a truth table is not enough to show input/output relationships because it ignores time.
The aid used in examining the time dependent aspect of a sequential network is called a timing diagram

## Slide 70: THE R-S FLIP -FLOP
It has 3 inputs S(Set), R (Reset) and C (a clock input) which synchronises the action of the flip-flop with its surrounding
The two outputs (Q and Q) are always in opposite states from each other.
Most significant changes occur when there is a clock transition.
If the clock input is constant, the outputs will follow the changes in the inputs at all times.
When the clock is in 0 state Both R and S inputs have no effect on the state of the flip-flop. The network is then stable. In this state, if Q = 1, Q is = 0 and Q is maintained at 1. If Q is 1, Q = 0 and Q is maintained at 1.
If the clock is raised to 1 the network will not change if R = S = 0
The subscripts Q- and Q- indicate outputs just before the clock becomes 1 and the subscripts Q+ and Q+ show outputs just after the clock becomes 1

## Slide 80: REGISTERS
Transfer of new information into the register is known as loading the register.
If all bits of the register are loaded at the same time we say that the loading is done in parallel.

## Slide 81: Shift registers
Shift registers are classified according to input and output which maybe either serial or parallel.
A serial input is one for which the input arrives 1 bit at a time, and each time a bit arrives the register is shifted by one to accommodate the new bit.
A parallel input is one for which the inputs are all loaded at the same time.
If the left most bit is brought around and put in the right bit during a left shift, or the right most bit is put in the left bit during a right shift the operation is called a rotation.

## Slide 82: Shift registers
The Shift Register is another type of sequential logic circuit that can be used for the storage or the transfer of binary data.
They are capable of shifting their bits either to the left or to the right. They have a tendency of rearranging their contents.
If an 8 bit register contains 0 1 1 0 0 1 0 1 and a left shift operation is performed, the new contents of the register will be;
1 1 0 0 1 0 1 0.
A 1 bit right shift would result into
0 0 1 1 0 0 1 0

## Slide 83: Example
Consider initially A = 01101001 and the carry flag (c) = 1

## Slide 87: Data Transmission
A transmission that is controlled by a common clock signal is said to be synchronous.
A transmission that is not controlled by a common clock signal is said to be asynchronous.
The logical 1 and logical 0 are respectively knows as the mark and space.