## Slide 1: Module 4
Communication Protocols

## Slide 2: Communication protocols
Communication protocols are a set of rules and conventions that define how data is transmitted and received between devices in a network.
They ensure that devices can communicate effectively and understand each other's messages.
They are essential for enabling devices to communicate and exchange information in a network.

## Slide 3: Basic Protocol Functions
Message Formatting
Protocols define the structure and format of messages exchanged between devices.
Addressing
Specifies how devices are identified within a network, using unique addresses.
Routing
Determines how data is forwarded from source to destination across a network.
Error Handling
Protocols include mechanisms for detecting and correcting errors in transmitted data.
Flow Control
Manages the rate of data transmission to prevent overwhelming the receiver.
Congestion Control
Prevents network congestion by regulating the flow of data.

## Slide 4: Principles of Internetworking
Interoperability:
Different networks can communicate with each other using standardized protocols.
Routing:
Efficient routing ensures data reaches its destination across interconnected networks.
Addressing:
Uniform addressing allows devices from different networks to be uniquely identified.
Encapsulation:
Data is encapsulated at each layer of the protocol stack for efficient transmission.
Gateways/Routers:
Connect networks with different protocols and ensure seamless communication.

## Slide 5: Internet Protocol
a. IPv4:
  Uses a 32-bit address, represented in dotted-decimal format (e.g., 192.168.1.1).
  Limited address space, leading to the adoption of IPv6.
b. IPv6:
  Uses a 128-bit address, providing a significantly larger address space.
  Designed to address the exhaustion of IPv4 addresses.
c. Addressing:
  IP provides a hierarchical addressing system to enable efficient routing.
  Divides the address space into network and host portions.
d. Routing:
  IP enables the routing of data packets across interconnected networks.
  Uses routing algorithms to determine the best path for data packets. Routers play a key role in forwarding packets between networks.

## Slide 6: Internet protocol
e. Fragmentation and Reassembly:
  IP allows for the fragmentation of large packets for transmission and reassembly at the destination.
  Enables the transmission of data over networks with varying maximum frame sizes.
f. Internet Control Message Protocol (ICMP):
  Part of the Internet Protocol suite, ICMP is used for error reporting and diagnostics.
  ICMP messages include error messages, echo requests and replies (ping), and network diagnostics.
  Helps identify and troubleshoot network-related issues.
g. Address Resolution Protocol (ARP):
  Resolves IP addresses to corresponding MAC addresses in a local network.
  ARP is used when a device needs to communicate with another device on the same local network.
  Maps IP addresses to MAC addresses by broadcasting ARP requests.
h. Sub-netting
  IP allows for the subdivision of large networks into smaller, more manageable subnets.
  Sub-netting improves network organization, security, and performance.

## Slide 7: Internet Protocol
h. Multicast and Anycast:
  IP supports multicast for one-to-many communication and anycast for one-to-nearest communication.
  Multicast allows a single sender to communicate with a selected group of receivers.
  Anycast enables the routing of data to the nearest of several potential receivers.
  Efficiently supports content delivery and load balancing.
i. Security (IPsec):
  IPsec (Internet Protocol Security) provides security features for IP communication.
  Ensures confidentiality, integrity, and authenticity of data exchanged between devices.
  Supports the creation of Virtual Private Networks (VPNs) for secure communication over the Internet.
  Implemented at the IP layer to secure all higher-layer protocols.
Notes: Understanding the intricacies of the Internet Protocol is fundamental for network administrators, engineers, and anyone involved in the design and management of IP-based networks. IP forms the basis for communication on the Internet and plays a crucial role in the functioning of modern networking systems.

## Slide 8: Collision Free Protocols
Collision-free protocols are designed to prevent or eliminate collisions. A collision occurs when two or more devices attempt to transmit data on a network simultaneously, resulting in data corruption.
Examples are:
  Time division multiple access/ Time division multiplexing (TDM).
  Frequency division multiple access/ Frequency division multiplexing (FDM).
  Code division multiple access/ Code division multiplexing (CDM).
  Wavelength division multiplexing (WDM).
  Statistical Time Division Multiplexing (STDM)
Multiplexing. Multiplexing is a technique used in networking and telecommunications to combine multiple signals or data streams into a single channel for transmission over a shared medium. The purpose of multiplexing is to make more efficient use of available resources, such as bandwidth or transmission lines.

## Slide 9: Time division Multiplexing
TDMA is a protocol used in networks to divide time into slots, and each node on the network is allocated a specific time slot during which it can transmit data.
For example: In satellite communication, different earth stations may transmit and receive data during their designated time slots.

## Slide 10: Frequency Division Multiplexing.
FDMA divides the available frequency spectrum into channels, and each node is allocated a specific frequency band for communication.
Since different nodes use different frequencies, there is no collision during simultaneous transmissions.
For example: Analog radio and television broadcasting often use FDMA. Each station is assigned a unique frequency for broadcasting.

## Slide 11: Code Division Multiplexing.
CDMA allows multiple nodes to transmit simultaneously over the same frequency band by using unique codes to differentiate between the signals.
Each node is assigned a unique code, and all nodes can transmit over the same frequency band concurrently. The receiver uses the corresponding code to distinguish and decode the signals.
For example: CDMA is widely used in mobile communication technologies, such as 3G and 4G/LTE.

## Slide 12: Wavelength Division Multiplexing
WDM is used in optical fiber communication to simultaneously transmit multiple signals over different wavelengths (colors of light).
Each wavelength represents an independent communication channel, allowing for high data rates and increased capacity.
WDM is a key technology in optical networking, enabling the high-speed transmission of data over long distances.

## Slide 13: Statistical Time Division Multiplexing (STDM)
STDM is an extension of TDM that allows for more flexible allocation of time slots based on demand.
Time slots are assigned dynamically to channels with data to transmit, providing better utilization of the available bandwidth.
STDM is commonly used in packet-switched networks and is more adaptive to varying data rates.

## Slide 14: Contention protocols
Contention protocols are used in computer networks to manage access to a shared communication channel where multiple devices contend for the opportunity to transmit data. These protocols handle situations where there is a possibility of collisions, and they determine how devices contend for access to the communication medium.
Examples are
  Carrier Sense Multiple Access
  Token Passing

## Slide 15: Carrier Sense Multiple Access
CSMA is a contention protocol that allows devices to listen to the communication channel before transmitting. If the channel is sensed as idle, the device can transmit its data.
There are two variants of CSMA:
  CSMA/CD (Collision Detection): Used in Ethernet networks. If a collision is detected during transmission, devices stop transmitting and initiate a back-off period before retrying.
  CSMA/CA (Collision Avoidance): Used in wireless networks like WI-FI. Devices listen for ongoing transmissions and try to avoid collisions by waiting for the channel to be clear.

## Slide 16: Token Passing
Token passing is a protocol where a special data packet, known as the token, circulates around the network. Only the device in possession of the token is allowed to transmit data.
The device with the token can transmit data, and after transmission, the token is passed to the next device.

## Slide 17: Media Access Protocols
CSMA/CD (Carrier Sense Multiple Access with Collision Detection):
  Used in Ethernet networks, devices contend for access to the communication medium, and collisions are detected.
Token Passing:
  Example: Token Ring network, where devices use a token for controlled access.
TDMA (Time Division Multiple Access):
  Divides the communication medium into time slots, with each assigned to a device.
CDMA (Code Division Multiple Access):
  Assigns a unique code to each device, allowing multiple devices to share the same frequency band simultaneously.