## Slide 1: Module 5
Data Communication and Transmission

## Slide 2: Concepts and Terminology
Data Communication
The process of exchanging data between two devices over a communication medium.
Communication Medium
The physical or logical path that facilitates the transfer of data between devices.
Data Transmission
The process of sending data from one device to another over a communication medium.
Bandwidth
The capacity of a communication channel to transmit data, measured in bits per second (bps).
Signal
A representation of data in a form suitable for transmission over a communication medium.

## Slide 3: Concepts and terminology
Modulation and Demodulation:
Modulation: This is the process of modifying a carrier signal to encode digital data for transmission.
Common modulation techniques include Amplitude Modulation (AM), Frequency Modulation (FM), and Phase Modulation (PM).
Demodulation: This is the process of extracting the original digital data from a modulated carrier signal.
Data Rate
The speed at which data is transmitted over a communication channel, measured in bits per second (bps).
Latency
The time delay between the initiation and completion of data transmission.

## Slide 4: Concepts and Terminologies
Throughput
The actual amount of data transmitted successfully over a communication channel in a given time period.
Propagation Delay
The time taken for a signal to travel from the sender to the receiver.
Attenuation
The decrease in signal strength as it travels through a medium.
Distortion
Alteration of the signal waveform during transmission, leading to signal degradation.
Noise
Unwanted interference that affects the quality of the transmitted signal.
Duplex Communication
Simultaneous two-way communication between two devices.

## Slide 5: Concepts and terminology
Half-Duplex
Communication in which data can be transmitted in both directions, but not simultaneously.
Full-Duplex
Simultaneous two-way communication, allowing data transmission in both directions simultaneously.
Protocol
A set of rules and conventions that govern the format and sequence of messages exchanged between devices.
Handshake
An initial communication process between devices to establish a connection and agree on communication parameters.
Bit Error Rate (BER)
The ratio of bits received in error to the total number of bits transmitted.
Jitter
Variability in the arrival time of data packets, affecting the regularity of data flow.

## Slide 6: Concepts and terminologies
QoS (Quality of Service)
The measure of the overall performance and reliability of a communication network.
Router
A network device that forwards data packets between different networks.
Switch
A network device that connects multiple devices within the same network and uses MAC addresses to forward data.
Gateway
A device that connects different networks with different communication protocols.
Firewall
A security device that monitors and controls incoming and outgoing network traffic based on predetermined security rules.
Range
This is the coverage area of a wireless signal or the distance over which devices can communicate effectively.

## Slide 7: Concepts and terminologies
Protocols at Different OSI Layers
  Application Layer Protocols: Examples include HTTP, FTP, SMTP.
  Transport Layer Protocols: Examples include TCP, UDP.
  Network Layer Protocols: Examples include IP, ICMP.
  Data Link Layer Protocols: Examples include Ethernet, PPP.
  Physical Layer Protocols: Examples include USB, Ethernet cables.
Packet
A small unit of data that is transmitted over a network.
Frame
A complete unit of data at the data link layer, including the packet and control information.
Frame Relay is a standardized wide-area network (WAN) protocol that operates at the data link layer (Layer 2) of the OSI model. It was designed to efficiently transport variable-sized data packets over digital networks.

## Slide 8: Guided and Unguided (Wireless) Transmission
Guided Transmission:
Data travels over a physical, wired medium (e.g., copper cables, fiber-optic cables).
Examples include twisted-pair cables and optical fibers.
Unguided (Wireless) Transmission:
Data travels through the air without the need for a physical medium.
Examples include Wi-Fi, Bluetooth, and cellular communication.

## Slide 9: Transmission Impairments and Errors
Transmission Impairments:
These are factors that affect the quality of data transmission.
Examples include attenuation, distortion, and noise.
Errors:
These are inaccuracies in transmitted data caused by various factors.
Error detection and correction techniques are employed to ensure data integrity.

## Slide 10: Forms of Transmission Impairment in Cables
(a) Attenuation
  Weakening of the signal strength as it travels through the cable.
  Causes
  Resistance in the conductors.
  Signal absorption by the cable material.
  Solutions:
  Signal amplification using repeaters.
  Use of low-loss cables.
(b) Distortion
  Alteration of the signal waveform during transmission.
  Causes:
  Signal reflection due to impedance mismatch.
  Non-uniform propagation speeds for different frequency components.
  Solutions:
  Proper cable termination to minimize reflections.
  Equalization techniques to compensate for frequency-dependent distortions.

## Slide 11: Noise
  Unwanted interference that degrades signal quality.
  Causes:
  Electromagnetic interference (EMI).
  Radio-frequency interference (RFI).
  Solutions:
  Shielding cables to reduce external interference.
  Use of twisted pair cables to minimize electromagnetic coupling.

## Slide 12: Solutions to Overcome Transmission Impairment
Signal Amplification
  Introduce signal amplifiers (repeaters) at intervals to boost weakened signals.
Equalization
  Use equalization techniques to compensate for frequency-dependent distortions and ensure signal integrity.
Proper Cable Termination
  Ensure proper termination of cables to minimize signal reflections and distortion.
Shielding
  Shield cables to reduce the impact of external electromagnetic interference (EMI).
Twisted Pair Cables
  Use twisted pair cables to minimize electromagnetic coupling and reduce the effects of radio-frequency interference (RFI).

## Slide 13: Analog and Digital Data Transmission
Analog Transmission
Represents data as continuous, varying signals.
Examples include analog phone lines and AM/FM radio.
Digital Transmission
Represents data as discrete, binary signals.
Examples include digital communication over the Internet.

## Slide 14: Analog data transmission
Examples
Analog data transmission is commonly found in traditional communication systems, such as:
  Analog audio signals in music and voice communication.
  Analog video signals in older television broadcasts.
  Analog signals in various sensor measurements (e.g., temperature, pressure).
Advantages
Suitable for representing natural, continuous phenomena.
Analog signals can provide a theoretically infinite range of values.
Disadvantages
Susceptible to signal degradation over long distances.
Prone to interference and noise, impacting signal quality.
Difficult to amplify or regenerate without introducing distortions.

## Slide 15: Digital data transmission
Examples
Digital data transmission is prevalent in modern communication systems, including:
  Digital audio signals in CDs and streaming platforms.
  Digital video signals in DVDs, Blue-rays, and streaming services.
  Digital data in computer networks and the internet.
Advantages:
Less susceptible to signal degradation over long distances.
Robust against noise and interference due to well-defined signal levels.
Facilitates error detection and correction mechanisms.
Challenges:
Limited precision compared to analog signals.
Requires higher bandwidth for the same amount of information carried by analog signals.
Signal processing introduces quantization errors.

## Slide 16: Circuit switching
In circuit switching, a dedicated communication path or circuit is established between two devices for the duration of their conversation.
The entire bandwidth of the communication path is reserved for the duration of the conversation, even if no data is being transmitted.
Traditional telephone networks (PSTN - Public Switched Telephone Network) often use circuit switching. When you make a phone call, a dedicated circuit is established for the duration of the call.

## Slide 17: Packet Switching
In packet switching, data is divided into small packets before transmission. These packets are then sent independently across the network and may take different routes to reach the destination.
Each packet contains information about its destination address, allowing routers in the network to make decisions about the best path for each packet.
The Internet is a notable example of a packet-switched network. TCP/IP (Transmission Control Protocol/Internet Protocol) is the suite of protocols commonly used for packet-switched communication.

## Slide 18: Message Switching
In message switching, the message is treated as a whole and is passed from one node to the next until it reaches its destination.
Unlike packet switching, where data is divided into smaller packets, message switching involves forwarding the entire message.

## Slide 19: Key differences between Circuit, Packet and Message Switching.
Resource Usage
  Circuit switching reserves resources for the entire duration of a conversation, even if no data is being transmitted.
  Packet switching allows for more efficient use of resources since bandwidth is shared among multiple conversations.
Flexibility
  Circuit switching provides a dedicated and predictable path but may not be as flexible in handling varying data rates or bursty traffic.
  Packet switching is more flexible, allowing for dynamic routing and adaptability to different traffic patterns.
Delay
  Circuit switching may introduce higher delays due to the setup time required to establish a dedicated path.
  Packet switching may have lower delays, especially in networks with low latency and efficient routing algorithms.

## Slide 20: Encoding
Encoding refers to methods used to represent information in a form that can be transmitted and interpreted reliably between devices.
Different encoding techniques are employed based on the type of information, the medium of transmission, and the requirements of the communication system.
Here are some common encoding techniques:
    Digital encoding
    Analog encoding
    Line encoding
    Modulation
    Pulse code modulation
    Run-length encoding
    Huffman coding
    Base64 encoding
    Quadrature amplitude modulation

## Slide 21: Digital encoding
Binary Encoding: In digital systems, information is often represented using binary digits (0s and 1s).
Each bit represents a binary value, and combinations of bits can represent characters, numbers, or other data.
Binary encoding is fundamental to all digital communication.

## Slide 22: Analog encoding.
Analog-to-Digital Conversion (ADC): Analog signals, which are continuous and can take any value, are converted into digital signals for digital communication systems. ADC transforms the analog signal into a discrete set of digital values.
Digital-to-Analog Conversion (DAC): In some cases, digital information needs to be converted back to analog form for transmission over analog mediums. DAC performs this conversion.

## Slide 23: Line encoding
Manchester Encoding: In Manchester encoding, each bit is represented by a transition from one voltage level to another within the middle of a bit period. This helps in clock synchronization.
Differential Manchester Encoding: Similar to Manchester encoding, but the presence or absence of a transition at the beginning of a bit period determines the bit value. It provides a self-clocking mechanism

## Slide 24: Advantages of Manchester encoding
Guaranteed bit transitions at regular intervals, aiding in clock recovery.
Provides a self-synchronizing mechanism.
Lower susceptibility to long runs of consecutive identical bits.
Disadvantages
Requires twice the bandwidth compared to NRZ encoding.
More complex encoding and decoding circuitry.

## Slide 25: Modulation
Amplitude Modulation (AM): In AM, the amplitude of a carrier signal is varied to encode information. It is commonly used in analog audio broadcasting.
Frequency Modulation (FM): In FM, the frequency of a carrier signal is varied to encode information. It is widely used in analog radio broadcasting.
Phase Modulation (PM): In PM, the phase of a carrier signal is varied to encode information. It is used in some forms of analog communication.

## Slide 26: Pulse code modulation
PCM is a method used to digitally represent analog signals.
The analog signal is sampled at regular intervals, and each sample is quantized and represented using a binary code.

## Slide 27: Run length encoding
RLE is a form of data compression where sequences of the same data value are stored as a single data value and count.
It is often used in image and video compression

## Slide 28: Multiplexing
Combining multiple signals for transmission over a single communication channel.
Types
  Time Division Multiplexing (TDM): Allocates time slots to different signals.
  Frequency Division Multiplexing (FDM): Allocates frequency bands to different signals.
  Code Division Multiplexing (CDM): Each signal is assigned a unique code for simultaneous transmission.